41’ UTB Study Guide

MK2 S.M. Dupre`

Underway Limits

- 10 hrs in seas under 4’

- 8 hrs in seas greater than 4’ less than 8’

- 6 hrs in night, reduced visibility, heavy weather

30 knot winds

8’ seas

No surf, breaking waves

100 gross tons for towing

Engine Knowledge

VT-903M

V block, turbo, 903 cubic inch, marine version

340 HP 318 shaft horse power

Four stroke, eight cylinders, right hand rotation

#2 diesel

Oil 15w40, 6gallons (5g sump, 1g lines/filter)

Jacket water – antifreeze: 12gallon, 50/50 mix, 2” from the top

Sink holds 20gallons of non-drinking water

Bilge pumps: 1300gph, 24V DC, starboard discharge, 3 alarms

Temps and PSI’s

IDLE			Cruise		MAX

Tach:	      	 	700-725 rpm		2300rpm	2700rpm

Engine Oil:		10-30psi		40-65psi

Marine Gear:		25-70 disengaged	190-220psi

Water Temp:		140 F to bring up	165-195 F	200+/-5

Audible Alarms

Low L/O pressure – Bell (12 psi)

High Water Temp – Bell ( 200 +/- 5)

Bilge Flood – Horn / Blue Light

Eng room thermal sensor – Horn (190F)

Alarm Lights

Alternator – RED

Low L/O Pressure – RED

High Water Temp – YELLOW

Fuel  System

Fuel Tanks: have striker plates for the sounding rods

Fuel Full – 486.8 	243.4 per tank

Fuel 95% - 463 	231.5 per tank

Fuel useable – 420	210 per tank

Check Valves on the return line

Priming and stripping pump: 5:1, 100 pumps =20 gallons

Marine Gear 509

Twin Disc INC.

40wt oil (9250)

11 qts, 10 in marine gear, 1 in the cooler

2:1 ratio

“COME HOME” device: STBD ENG only ¼ turns on allen screws

Selector Valve: port side upside down

Shaft: 9’ by 2” diameter, Armco Aqua met 17 corrosion resistant steel, penetrates at frame10

Shaft Packing: 6-10 drops per minute

Propellers: Two 26” diameter by 28” pitch nickel- aluminum- bronze alloy, grade 4 and 4 bladed. Rotate outboard

* Main Propulsion Cooling System:

Sea Chest: 3 min. before impeller burns out

Sea Chest Vent: STBD of tow reel

Duplex Strainer: 2 ½”

Raw Water Pump: 60 GPM

Heat Exchanger ( M/G Cooler ( Exhaust Riser ( Flexible Flange ( Deicing Valves & Lines ( Muffler

Muffler: Cools and muffles the sound of the exhaust

*Jacket Water Cooling and Heating System:

12 Gallon system 50/50 glycol antifreeze

Jacket Water Pump ( Heat Exchanger ( Defroster (STBD) Heater (PORT) ( L/O Cooler ( Hot Start

*Lubricating Oil System:

Oil 15w40 6 gallons (5g slumps 1g filters)

L/O Pump ( L/O Cooler ( L/O Filter:

Dip sticks: Starboard side are the most difficult to deal with.

*Steering System:

Steering Wheel: Morse, Non-magnetic 20” wheel

Hydraulic ram via two hoses

Tie Rod Bar: 1” w/ bronze ends and quick push pins.

Rudder Arms: Bronze

Rudder Post: Armco Aqua met 17 corrosion resistant steel

Rudder Blade: 316 stainless steel

Rudder Stop: Port side

*Electrical:

Batteries: Two 12V, 200 amps, series connected to produce 24 volts DC

110V AC Breaker: Receives power from the 110V shore-tie for the hot starts, 110V battery charger, heater and receptacles

12V DC Breaker: Receives power from the batteries through a 12V battery equalizer for the elect nav equipment. Have a voltmeter on the left and an ammeter on the right.

24/28V DC Breaker: Receives power from the batteries for alarms, horn, lights, Delco-Remy starters and console display panel. Have a voltmeter on the left and an ammeter on the right.

Alternators: Prestolite, 24 volt, 75 amps, output - 28.4 volts

*FIRE EXTINGUISHING SYSTEMS:

Halon 1301 Bottle: set off for 5 min, vent for 15 min

CO2 Bottle 5 lbs: 4-6 feet

2 PKP Bottles 10 lbs: 8-12 feet, purple potassium bicarbonate

Thermal Sensors: Alarm goes off at 190 degrees; there are two of them located behind the engines, aft of the hatches

Fuel Shut-off Cylinder

Fire Main System: 250 gpm at 80-100 psi

PTO: Power take off, 1000 max rpm

Sea Chest ( Simplex Strainer ( Fire Pump ( Fire Main Riser ( Wyes-gate

Vari-nozle: 1 ½”

Hoses: 1 ½” X 25’ & 50’, 2 ½” X 12’ & 30’

Eductor: 250gpm input, 500gpm out put and a 20’ lift

P6: 250 gpm, 12’ lift, 1g gas, 2.5-4.5 hours, 120 pounds

Alpha: Natural material

Bravo: Chemical

Charlie: Electrical

Delta: Metal

*STARTING PROCEDURES:

Check bilges for liquids

Check oils, fuel (at or near 95%), coolant (2” below fill neck) & tension on belts (no more than 7/16” per foot).

Check fuel valves and open sea-chest valves.

Secure shore-tie power at the pier breaker, and remove shore-tie plug.

Ensure breakers 11, 12 (starters) & 17(engine alarms) are ON.

Turn the engine alarm bell toggle switches ON.

Ensure Morse throttles are in neutral.

Push down on fuel stop T-Handles.

Depress engine starter buttons until started, but no longer than 30 seconds every 2 minutes.

Check gauges for proper readings

Check raw water discharge

# BASIC ENGINEERING CASUALTY CONTROL EXERICISES (BECCE)

High Water Temperature: Clutch on throttles; affected engine identified; crew briefed; engine secured if temperature rises; overboard checked; engineer checks through port hole then enters the engine room to check for sea suction valves open, sea strainers clean, cool lines ok, bilges checked, raw water pump and expansion tank checked after cooled down; station notified.

Loss Of Lube Oil Pressure: Clutch on throttles; affected engine identified and secured; crew briefed; engineer checks port hole then engine room looking for oil in bilge and for oil in engine; ; crew member rig anchor in needed and acts as safety observer with fire extinguisher; station notified; RTB in unable to repair.

Collision W/ A Submerged Object: Neutral on throttles; crew briefed; cox’n verified position; engineer checks engine room, crew man checks all other compartments; reduce flooding if needed; engines checked and checked for vibration; notify station.

Loss Of Steering (Cable/ Hydraulics): Clutch & steer with throttles; notify crew; engineer investigate, crew member rig anchor if needed & provide tiller; throttles in neutral; tiller stepped on port side; detach pin on stbd post & test range on motion; notify station.

Loss Of Steering (Jammed Rudder): Clutch & steer with throttles; notify crew; engineer investigate, crew member rig anchor if needed & provide tiller; throttles in neutral; tiller stepped on port side; engineer remove tie rod bar if needed to find jammed rudder; try to free rudder if unable secure rudder; notify station.

Fire in the Engine Room: Neutral on throttles secure engines; engineer checks through port hole; station contacted; write down position; cox’n gives OK to energize Halon 1301 and mark time; electric power secured, crew member rig anchor and lift raft moved forward if needed.

Shaft Packing Overheat: Clutch on throttles, do not disengage shafts or secure engines, cool down shafts and packing glands with raw water, then loosen packing gland nut.

Loss of Reduction Gear: Neutral on throttles, check marine gear oil pressure gauge for affected side, if zero then secure that engine immediately.

Runaway Engine: Clutch on both throttles, if engine continues to runaway pull the T-handle on the effected engine, if engine continues to runaway place unaffected engine in neutral and turn in the direction of the runaway engine to increase shaft load.

*41’ SPECIFICATION:

Length:  ____________41’03 ¾”

Length molded: ______40’08

Beam: _____________14’01”

Beam molded: _______13’05 ¼“

Freeboard bow: ______4’06”

Freeboard F7: _______3’09”

Freeboard stern: _____2’09”

Max Draft: _________4’01”

Height of radar: ______13’02”

Height of mast: ______17’

Height of antenna: ____26’08”

Max speed: __________26 knots

Endurance @ MS: ____10.5 hours

Range @ 2000rpm: ____300 NM

Displacement, full: ____30,000 pounds

Displacement, less: ____26,000 pounds

Crew min: ___________3

Crew max: __________ 20

Towing: ____________ 100 gross tons and less

Fuel: _______________ #2 Diesel

Longitudinal frames: ___ 11”

Transversal frames: ____ 31”

Gunwale to the Chine: __ 3/16”

Chine to the Keel: _____ 1/4”

Frame 11 to 13: _______5/16”

Tempered Glass: ______ 3/8”

Cleats: ______________ 15”

Tow Line: ___________ 600’ of 2 ¾” DBN; 17,015 pounds BS

Mooring Lines: _______ 2 X 30’, 2 X 60’ of 2 ¾” DBN

Line: _______________ 150’ and less

Cabin Top is a fiberglass reinforced plastic over an end-grain balsa core.

Can go from full ahead to full astern in 3-4 seconds and stop w/in 70 ft.

*MAST NAV LIGHTS:

Anchor – white - 360

Stern – white - 135

Masthead – white - 225

Towing – yellow - 135

2nd Mast – white – 225

### 2nd Tow - yellow – 135

# *COMPARTMENTS & HULL REFERENCES:

Forepeak: Watertight, Bow -F2

Passenger Compartment: Not watertight, F2 – F6

Engine Room: Watertight to the main deck, F6 – F10

Fuel Tanks: Watertight to well-deck, F10 – F11

Aft Lazarette: Watertight, F11-F13

F2: Docking lights

F6: Pivot point

F6-F7: Depth finder, 18” strb of keel.

F9: Max draft

F10: Shafts penetrate hull.

F12: Propellers are 2” from the water line.

*LEAD LINE:

2F: 2 leather

3F: 3 leather

5F: 1 white rag

7F: 1 red rag

10F: 1 leather

13F: 3 leather

15F:1 white rage

17F: 1red rag

20F: 2 knots

26F: 1 knot

Lead is 7-14 pounds

*DAMAGE CONTROL KIT:

Various sizes of hose clamps

Canvas, 4' x 4' sheet

Rubber gasket material, 4' x 4' x 1/8" sheet

Various sizes and number of wedges

Various sizes and number of plugs

Marline, 250' line

Oakum

Small ball of marlin

Wooden mallet

Hacksaw (with sheath) and spare blades

# *TOWING:

Scope: The length of the towline measured from bitt to bitt.

Catenary: The dip in the towline caused by the natural weight of the line; acts as a shock absorber

In Step: Both vessels riding the seas in the same relative position

Yawing: When the towed vessel veers from one side to the other.

Line one and four are spring lines, line two take forward strain & line 3 takes stern strain

Four turns on the towline reel should be left at all times

Use either a Double-Becket bend or Bowline when using a pennant.

41’ can tow up to 100 gross ton, about an 80’ vsl

# *ANCHORING:

*41 ANCHOR SPECS:

Anchor line: 300’ of 2 ¾“DBN line

¾” thimble

5/8 screw pin shackle

½” swivel

9’ of ½” BBB chain

7/16” screw pin shackle

# 25 lbs Dan forth anchor

Short stay: Situation when the anchor has been hove in just short of breaking free from the bottom.

Anchors aweigh: Lifted clear of the bottom.

Anchor in sight: First sited in water.

Up and down: Line is straight up and still on bottom.

Anchor is clear: Anchor clean.

Anchor is fouled: Anchor has debris or is tangled.

Anchor is shod: Covered with mud

Anchor rode: The line from the boat to the anchor usually made up of line plus a short of chain.

Scope of anchor rode: 5:1 & 7:1 for calm, 10:1 for heavy weather. (Exp: 100’ rode for 10’ water)

Make fixes to insure you’re not dragging your anchor.

*Survival Vest:

Signaling Mirror: Infinity distance to attract boats and planes

Signaling Whistle: Heard up to 1000 meters/ 1100 yards

MK 124: Orange smoke/ red flare, lasts 20 seconds each sides, ribbed on night side, with a surgeons knot, use at a 45 degree angle w/ thumb

MK 79:

MK 31: 7 Red star flares, 250- 650 feet, 12000 candle power for 4.5 sec

MK 80: Pencil type projector

Signaling Light: Aka Firefly, 50+/- 10 flashes per minute, 100,000 candle power,  9 hours continuously, 18 hours intermediately, minimum 5 miles

Survival Knife: It’s a knife

PML: Personal Marker Light, seen up to 1 mile, lasts 8-12 hours

MK 127A1: Parachute white star flare, 650-700 ft, 36 sec of burn, 125000 candle power, descends 10-15 ft per sec

*EGRESS ROUTE:

Emergency escape hatch

Port side window

Starboard side window

Rear window door

# *NAVIGATION:

Variation: the angular difference between true north and magnetic north measured in degrees

Deviation: the magnetic influences of the vessel and the electronics on the compass (recorded every 15 degrees)

Uncorrected: TVMDCAW True Variation Magnetic Deviation Compass Add West

True virgins make dull companions at weddings

Corrected: CDMVTAE Compass Deviation Magnetic Variation True Add East

Can Dead Men Vote Twice At Election

True direction is the outer ring and Magnetic direction is the inner ring of a compass rose.

Fixes: is a form of latitude and longitude from a GPS plotted on a chart; intersection of two or more bearing lines on fixed objects or radar bearing and/or ranges from prominent point of land or objects with a spread of 60 degrees or greater. 3NM and in, fixes shall be taken every 15 min, 3NM and out fixes shall be taken every 30 min.

Square: Estimated position

Triangle: Electronic fix

Circle: Visual fix

Semi-Circle: Dead reckoning

Estimated Position: (EP) is a DR but modified by additional info, which in itself is insufficient to establish a fix; such as radar ranges and/or bearing on one floating aid, passing abeam a ATON w/ out an established radar range or bearing,

Dead Reckoning: (DR) Approximant position by determining its speed, time and its course are done every ½ hour, speed and course change. Marked by a half circle

Lines of Position: (LOP) two or more compass bearings 60-120 degrees to locate your position

Meridian of Longitude: Is a great circle formed by planes which cut through the earth’s axis and its poles. They run North and South and are measured east to West on the top and bottom of a chart.

Parallels of Latitude: Are circles that run from the equator to the poles. They run East and West and are measured north to South on the sides of the chart and are measurable.

200 yrd = .1NM

2000 yrd = 1NM

1degree = 60NM

1 minute = 1NM

1 sec = 33.33 yrd

Distance = Nautical Miles 60 x D

Time = Minutes S x T

Speed = Knots time decimal x 60

Three minute rule: Distance traveled in yards in three minutes divided by 100 = speed in kts

Six minute rule: Distance traveled in NM in six minutes times 10 = speed in kts

The compass rose is magenta in color for the use of a red light; magnetic in side, true outside.

Slanted lettering on a chart means floating ATON.

Darker blue is shallow water, white is deep water.

# *NAVRULS:

# MANEUVERING SIGNALS

0 : I’m altering course to starboard / (inland) port to port passing

00 : I’m altering course to port/ (inland) starboard to starboard passing

000 : Astern propulsion

--- --- 0 : I intend to overtake you on your starboard side

--- --- 00 : I intend to overtake you on your port side

--- 0 --- 0 : Agreement to overtake signal

00000 : Danger

--- : Blind bends and departing dock

RESTRICTED VISIBLILITY

Vessels under 12 meters must have a sound producing device,

Vessel 12 – 100 meters must have a whistle and bell,

Vessel over 100 meters must have a whistle, bell and gong

Vessels U/W must sound signals at intervals of not more than 2 minutes

--- : Power-driven vsl U/W making way

--- --- : Power-driven vsl U/W not making way

--- 00 : Vsl towing, fishing, restricted maneuverability, constrained draft, sailing & not under command

--- 000 : Manned vsl being towed

--- 0 --- : Additional sound when at anchor to give away her position.

0000 : Pilot vsl at any time

Vessels anchored in R/V must sound signals at intervals of not more than 1 minute.

Vessels less than 100 meters a rapid bell ringing for 5 seconds.

Vessels more than 100 meters a rapid bell ringing for 5 seconds followed by a rapid gong ringing for 5 seconds.

If vsl is aground three distinct strokes of the bell before and after the ringing of the bell shall be applied.

*LIGHTS:

Special flashing light is Yellow and 50-70 flashes per min

Blue flashing: Law Enforcement

Yellow in 3s: Submarine

3 Greens: Mine Sweepers

Red over White over Red: Restricted in her ability to maneuver

Red and Yellow flashing: Medical or Fire Dept

Red over White: Fishing

Green over White: Trawling

White over Red: Pilot

Red over Red: Not under command or aground if no side lights

Red over Red over Red: Constrained by draft

Red over Green: Sailing vsl

Red, Green and White: Sailing vsl under 20M

White: Anchored or sailing vsl under 7M

White over White: Towing

White over White over White: Towing

Yellow over Yellow: Towing

Side lights:…112.5

Stern:……….135

Mast:……….225

Anchor:…….360

*RIGHT OF WAY:

(Non Rates Can Fool Some Petty-officers Sometimes)

Not under command

Restricted in her ability to maneuver

Constrained by draft

Fishing

Sailing

Power driven vessel

Seaplane

*DISTRESSES:

Red star shells

Parachute red flare

Flashing white light 50-70 per min

Smoke

Flames on a vessel

Gun fired at intervals of 1 min

Dye marker

Waving arms

Orange background black ball and square

Square flag and ball

November Charlie flags

“Mayday” by radio

SOS _ _ _ . . . _ _ _

Fog horn continuous sounding

EPIRB

Radio-telegraph alarm

Radio-telephone alarm

*ATON:

Red Right Return: Red nuns/ day boards shall be passed on the starboard when returning from sea. (Even #)

Green cans/ day boards to the port upstream. (Odd #)

Yellow buoys are special markers

Red and White buoys are safe water

# Black and Red buoys are danger

Blue and White buoys are mooring areas

Yellow triangles on the starboard & squares on the port, means you’re in the ICW heading upstream

# *FACTORS AFFECTING BOAT HANDLING:

### DYNAMIC FORCES

Wind: Acts on the vessels superstructure and hull

Set: Direction toward which water in flowing commonly measured in True degrees

Drift: Currents, wind and waves velocity measured in knots

Windward: Side or direction from which the wind is blowing

Leeward: Side or direction away from the wind

Seas: Ripples, waves, swells and surf

Pitching: Up/down motion of bow/stern (run at 45 degrees to correct)

Rolling: Side to side motion (run at 45 degrees to correct)

Yawing/Surfing: Tendency to rush from crest to trough of a wave causing the bow to dig in and the rudders lose grip

Flooding Tide: The tidal current flowing from sea toward the shore, results in higher tidal stages

Ebb Tide: Tidal current flowing from shore to sea, results in lower tidal stages

Slack Tide: The period of no horizontal movement

Eddy Current: Occur at channel bends, uneven bottoms and near points of land.

Radiation Fog: Cooled air below the dew point in the morning creates fog near water, sun burns it away.

Advection Fog: Warm air moving over colder land/water, sun has little effect, slight breezes make it denser.

Inlet: bay or river

Bars: A sand, mud, or debris shoal that crosses the mouth of a river or harbor

Breakers: A breaking wave

Comber: A wave about to break

Feathering: A thin line of white water on a comber

Surf: Several breakers in a continuous line.

Swells: Waves that have moved away from where they were created. (Like really big ripples)

Seas: Combination of waves and swells.

Trough: Valley between waves

Saddle: In the trough on the back part of a wave. (Best place to be when heading in toward land)

Fetch: Area where seas are generated by wind

Frequency/Period: Time between successive waves passing a fixed point.

### *CONSTRUCTION/ PROPULSION SYSTEM:

Pitch: Distance a propeller would travel in 1 revolution if advanced in a solid

Slip: Difference in distance of solid vs. fluid

Dynamic Pressure: Suction Screw Current: Water flow pattern into the propeller (low pressure)

Suction Screw Discharge: Thrusted water flow pattern out of the propeller (high pressure)

Side Force/Prop Walk: Stern moves sideways due to unequal blade trust, causing the shaft/propeller to push to the stern slightly sideways.

Unequal Blade Thrust: Pressure difference between the ascending and descending blades

Clockwise blade trust: stern walking to the starboard and bow turning port

Cavitation: Partial creation of a vacuum around the propeller forming air bubbles

Boundary Layer: Layer of water, varying in thickness, from the bow to stern

Frictional Wake: Caused by interference of the boundary layer by the propeller

Bank Cushion: Water between the bow and a near bank causing the bow to be pushed away from the bank

Bank Suction: Unbalanced pressure of water on the aft quarter forcing the stern toward the bank.

Displacement Hull: Displaces water at all times

Semi-Displacement Hull: Displaces water when at rest and raises when speed is increased

Planing Hull: Displaces water at rest and skims surface at speed

Keel: Back bone of the boat, runs fore and aft

Bare Keel: Extends below boats bottom to protect from grounding, increases draft

Flat/Flat Plate Keel: Built within the boats hull

Transverse Frames: The ribs of the boat, they run from side to side

Longitudinal Frames: Parallel to the keel

Rudders: Balanced, semi-balanced & unbalanced

Advance and Transfer: Vsl will continue slowly forward while graining ground turning to a direction.

# *VESSEL STABILITY:

Stability: Ability of a boat to maintain and return to an even keel determined by weight and buoyancy

Longitudinal Stability: Fore and aft, keeps boat from rolling end over end

Transverse Stability: Athwart ship, keeps from rolling over on its side and capsizing

Weight: Pushes vessel down in water

Buoyancy: Force pushes up from the water to keep vessel afloat

Center Of Gravity: Point at which the weight of the boat acts vertically downward, fixed unless change of weight

Force of Buoyancy: Upward thrust of water displaced by the hull

Equilibrium: Boat is at rest and the center of buoyancy is upwards in line with the center of gravity (balanced)

Rolling: The force of the center of gravity will move in the same direction as the roll (side to side)

Heeling: The underwater volume changes, causing a temporary leaning

Listing: A permanent leaning

Static Force: Caused by the placement of weight within the hull

Dynamic Force: Caused by the actions outside the hull, such as wind and seas

Gross Tons: Entire cubic capacity of a boat expressed in tons of 100 cubic feet.

Net Tons: Carrying capacity of a boat expressed in tons of 100 cubic feet

Dead Weight: Difference between the max loaded (cargo, fuel, etc.) and light displacement measured in long tons.

*Discrepancies:

Disabling: Casualties that make the boat not serviceable

----- Engine Parameters

Red Gear pressure below 190 psi

Engine Lube Oil pressure below 30 psi

Engine Jacket Water temp below 140F or above 212F

Engine Speed less than 2400 rpm’s or above 2900 rpm’s

----- Engine System Components

Engine fails to start

Uncontrollable overheats

Metallic/non-metallic: metal on metal, fuel knock, bearing, clicking

Excessive shaft or engine vibration

Engine surging, over speed (over 50 rpm’s)

Loss of engine governor control

Red gear fails to engage, FWD / REV

Fuel oil dilution 5% or greater

Water in Lube Oil

Lube oil in jacket water

More than a light sheen

Floating unmixed lube oil separated from the water

Alternator failure

Continuous electrical breaker trip

Starting batteries won’t charge

Steering system inoperative

Engine motor, mount hardware loose or missing

Excessive shaft packing leak

Packing while rotating trickle or steady stream

Packing while not rotating more than 15 drops per minute

----- Electronic / Navigation

No electronic means of signaling distress

Electronics won’t energize

Any fuel or oil drop falling on a hot surface

Electrical arching and sparking

Turbo charger lube oil suppy line leaking on hot surface or not fire rated/fire sleeve

Return fuel line leaking in the vicinity of the turbocharger where the turbo attaches to the saddle

Halon system inoperative, pressure below 425 psi

No fire extinguishers

Emergency alarms inoperative, fire, bilge, lube oil pressure, high water temp.

----- General

Hull breach below the water line

Inoperative sea chest valve

Restrictive: Casualties that restrict the operations of the boat such that it can perform some missions, but not all missions safely.

----- Engine Parameters

Engine speed less than 2575 rpm’s

Red Gear pressure greater than 225 psi

Water temp greater than 205 F

----- Engineering System Components

Leaks greater than 15 drops per minute

Antifreeze / jacket water

Raw water

Lube Oil

Hydraulic Oil

Red Gear Oil

Fuel Tank access cover

Fuel oil dripping on any surface that is not hot within 10 minutes

Bilge system valves installed incorrectly or missing

Bilge pump inoperative

Inoperative / inaccurate gauges

Engine pressure / Temp gauges

Any detectable exhaust leak

Fuel shut off valves do not fully close

PTO locking device missing or allows engagement

Missing or loose shafting bolts

Fire pump fails to engage

----- Electronics / Navigation

Compass deviation table missing, compass deviation greater than 5 degrees

VHF – FM inoperative

Depth finder inoperative

GPS inoperative

Radar inoperative

Nav lights inoperative, incorrect configuration

----- Safety

Missile hazard / obstruction of egress route

Fire extinguisher not secured in bracket

Underweight halon, with less than 42 psi or 42 LBS

Missing exhaust lagging or system blankets

----- General

Breach of watertight integrity

Failure of watertight closure to seal, cracks through a watertight scuttle / hatch