THESE ARE NOT THE TESTS! STUDY GUIDES ONLY!

SOME QUESTIONS ARE WRITTEN DIFFERENTLY AND SOME ARE WRITTEN BACKWARDS. IN OTHER WORDS, THE ACTUAL TEST QUESTION MAY ASK FOR WHICH ONE IS NOT THE ANSWER.

TEST 1

What is the reporting interval for the following reports?

Boat inspection report â€“ yearly

Cutter Engineering report-one year ending Dec 31

List the command that each of the following reports must be submitted to:

Boat Inspection Report â€“ MLC

Cutter Engineering Report â€“ MLC

A cutter engineering report uses what form?

CG-4874

Guidelines for reports are taken from what publication?

COMDTINST M9000.6 (series)

Where is the Boat Inspection Report copies sent to?

MLC

Where is the Cutter Engineering Report copies sent to?

MLC

The following units are required to maintain a Machinery History File.

All cutters 65 feet and longer.

What length vessels use a Boat Inspection Report?

65â€™ and shorter

Which types of vessels are required to maintain CSMP files?

Cutters 65â€™ and longer

What type of message identifies parts required to repair an equipment casualty?

CASREP

What priority code should be used on an SSMR for a shore station maintenance project that has to be completed within a 6-month period?

Priority 2

CSMP Priority:

1-URGENT. Items required to maintain operational capability, involve cutter or personnel safety, or are required by directives

Clear, understandable terms the work to be done in developing or producing the goods to be delivered or services to be performed by a contractor are included in what?

Statement of Work

Which of the following directives prescribes polices and procedures for administering the Coast Guard paperwork management program?

COMDTINST M5212.12 (series)

What is the reporting interval for the Cutter Engineering Report?

Every calendar year ending Dec 31

A Casualty Report (CASREP) should be submitted for any equipment malfunction or deficiency that cannot be corrected within 48 hours and affects the unit's _____.

primary and secondary missions

Units shall submit a CASREP as soon as possible, but not later than 24 hours, after the occurrence of a significant casualty which cannot be corrected within ____.

48 hours

Casualty Category 2 - A deficiency exists in mission essential equipment that causes a minor degradation of any primary mission, or a major degradation or total loss of a secondary mission

Casualty Category 3 - A deficiency exists in mission essential equipment that causes a major degradation but not the loss of a primary mission.

Casualty Category 4 - A deficiency exists in mission essential equipment that is worse than casualty category 3, and causes a loss of at least one primary mission.

What is the form number for a Shore Station Maintenance Record (SSMR)?

CG-4094

What priority code should be used on an SSMR for a shore station maintenance project that has to be completed within a 6-month period?

Priority 2

Which manual publishes the complete list of Coast Guard directives and their required distribution?

Directives, Publications and Reports Index

What Chapter/Section of the DPRI listing identifies the order form to use to request updates, replacements, or new directives?

Chapter 1, Section C

Where should you log the official changes issued to a directive?

Record of Changes Page

A Casualty Report (CASREP) should be submitted for any equipment malfunction or deficiency that cannot be corrected within 48 hours and affects the unit's _____.

primary and secondary missions

What priority code should you use on an SSMR for a shore station maintenance project that is to be accomplished as part of a normal backlog?

Priority 3

The Statement of Work is used to measure _____ performance

contractor

What is the form number for submitting an SSMR? CG-4094

What is used to cleaning the tubes in a shell and tube heat exchanger?

Nylon brushes

What type of brush is used for cleaning the plates in a plate type heat exchanger?

Fiber brush

What are the two types of auxiliary boilers?

Firetube and Watertube

When cleaning the tube sheet and inside shell of a heat exchanger, use a stiff _____ brush or plastic scraper.

Nonmetallic

What is the liquid called that results from saturated steam giving up its heat?

Condensate

What are the two basic types of OWS?

Vacuum gravity and pressure

What are the two types of AC motors?

Induction and synchronous

Which type of AC motor is MOST widely used today?

Single-phase induction

Which directive contains a list of the electrical safety precautions pertaining to working on AC motors?

NSTM, Chapter 300

What is always completed before training begins?

A safety walkthrough

Upon completion of an overhaul, the supervisor will ensure the completion is documented (entered) in to what two reporting systems?

Next Cutter Engineering Report, CMplus.

What supports shafting on the inside of the shipâ€™s skin?

Line shaft bearings

A directive is defined as ___________________________________.

A military communication in which policy is established or a specific action is ordered, a plan issued with a view to putting it into effect when so directed, or in the event that a stated contingency arises, and broadly speaking, any communication which initiates or governs action, conduct, or procedure

Which manual publishes the complete list of Coast Guard units and their distribution symbols?

SDL Standard Dist. List

What is the form # for the Boat Inspection Report?

CG Form 3022

The GAR evaluation scale uses what type of coding?

Color

Prior to starting the drill/exercise brief, a _______________________must be completed.

Safety walk through

Clean the tube sheet and the inside of the shell using fresh water and either a ___________or a plastic scraper.

Stiff nonmetallic brush

Back flushing is only required for _____________ plate type heat exchangers

Seawater-cooled

Remove the plates, tilt them toward the rear of the unit until the top slot is free of the_________________, and lift them out.

Guide bar

The disadvantages of a watertube boiler are:

Requires more maintenance, Expensive to build.

The temperature at which water boils is called the boiling point or

Saturation temperature

As saturated steam gives up its heat, the steam returns back to its liquid state. This liquid is called ______________.

Condensate

Boiler fuel nozzles will have a set of numbers stamped on the body. The first number indicates the amount of fuel _____________.

Which passes through in gallons per hour

Mark the position of the air damper on the blower casing for future reference

Scribe it

If you have an OWS that does not discharge oil, it could be the ____________________ or the ___________________.

Probe amplifier relay or the oil sensing probe

If an electric motor will not start, check the __________________.

Capacitor

What are the two basic types of OWS?

Pressurized; Vacuum/gravity

On what principle does an OWS operate?

Coalescing

Name three types of coalescing media that improve the efficiency of oil removal.

Metal plates, replaceable filters, and brush assemblies.

What component employs an optical system based on the principles of light scattering?

Oil content detector

A faulty sensing module can affect the __________ of water or accumulated oil.

Discharge

The â€œclean water inletâ€ and â€œclean water outletâ€ are what type of valves?

Solenoid valves

How often should the feedwater supply system be tested?

Daily

What is the MOST common type of AC motor used in industrial motion control systems?

AC Induction motor

What information is NOT found on the nameplate data label?

Torque

What type of switch is an electromechanical device that requires physical contact between the target object and switch activator?

Limit

When cleaning the tube sheet and inside shell of a heat exchanger, use a stiff _____ brush or plastic scraper.

Nonmetallic

When cleaning a plate-type heat exchanger, you should use caution when handling the plates because _____.

The edges can be very sharp and may cause injury

Who is responsible for ordering flexible hoses, gauges, and consumable used to overhaul an internal combustion engine?

The supervisor

Upon completion of an overhaul, what two reporting systems are used?

Next cutter engineering report, CMPlus

Characterized by the presence of fine abrasives in lubricants:

Bearing wear causing looseness without apparent surface degradation

Characterized by improper functioning of a torsion vibration dampener:

Bent or broken crankshaft

What supports shafting on the inside of the shipâ€™s skin?

Line shaft bearings

The sections of shafting outside the skin of the ship are usually supported with_____.

bearings

Under what circumstances can a gear with an overheated bearing be allowed to operate?

Only under extreme emergencies

What power transmission component in a propulsion system transmits power

from the DRIVING UNIT to the DRIVEN UNIT?

The marine propulsion unit

During which stage of an overhaul should a supervisor order all consumables required to complete the task?

Planning

What type of shaft is supported by the line shaft spring bearing?

Shafting inside the ships skin

A satisfactory contact percentage of gear tooth bearing contacting across the axial length of the working surface is _____ percent.

80

________________IS CAUSED BY EXCESSIVE OIL CONSUMPTION, OR EXCESSIVE CYLINDER CLEARANCE.

PISTONSLAP

A BRIGHT SPOT ON EACH END OF A PISTON RING IS CAUSED BY?

INSUFFICIENTRINGGAP

ON TUBE HEAT EXCHANGERS, THE FIN IS DESIGNED TO?

INCREASESURFACECONTACT

BOAT INSPECTION REPORTS ARE COMPLETED FOR VESSEL ___?

UNDER 65â€™

Edition 4, Test Number 52 I didnâ€™t have the opportunity to study after the test on this one, consequently, most of it ran out of my brain before I could go through the course materials.

What establishes policies, procedures, and standards for the administration of the Coast Guard Directives System for both Headquarters and the field?

COMDTINST M5215.6 (series)

Technical publications are maintained as reference materials and fall under the general

category of a _________________.

DIRECTIVE

The piston on the left has a surface area of four square inches. The piston on the right has a surface area of 40 square inches. If 20 lbs of pressure is applied to the piston on the left, how much weight will the piston on the right support? (UNDERSTAND THE MATH)

200

Propulsion machinery

The supervisor will be responsible for ensuring flexible hoses, valves, gauges, and all consumable items required for the overhaul are ordered.

Guidance for these tests, inspections, and break-in procedures should be contained in the appropriate overhaul MPC or technical publications, or as directed by the OEM technical representative.

Inadequate lubrication will not only cause piston wear, the extra friction may also:

cause piston seizure, land breakage, and piston pin bushing wear.

The major factor influencing shaft and bearing alignment is:

HULL DEFLECTION, VARIOUS LOAD AND BALLAST CONDITIONS, HULL SPEEDS, HEAVY SEAS.

Angular Alignment: 0.0005 inches per inch of companion flange diameter on a gap difference basis.

Remedies for â€œlow oil pressureâ€:

Partially clogged oil strainer, damaged or worn oil pump

Remedies for â€œno oil pressureâ€

Low oil level or empty sump, fully clogged oil strainer, or damaged or worn oil pump assembly

Auxiliary Equipment

The three most common types of heat exchangers used in the Coast Guard:

Shell and tube, fin and tube, plate type

A fin and tube heat exchanger is an air-cooled condenser used in AC&R systems

The fins increase surface area and aid in transferring heat.

A plate type heat exchanger is made up of parallel metal plates separated by gaskets

Plate type heat exchangers are used for cooling jacket water and lubricating oil in internal combustion engines and marine gas turbines.

Advantages of firetube boilers are:

- inexpensive to build

- simple to operate

-less maintenance

Disadvantages of firetube boilers are:

- long warm-up time

- weight of unit compared to the amount of steam producted

Advantages of watertube boiler:

- less warm up time

- ratio of size and weight to steam produced

Disadvantages of watertube boiler:

- requires more maintenance

- expensive to build

A float switch is installed on the tank to prevent the pump motor and solenoid valve from becoming energized in the event the condensate tank water level is low.

There are three general warning/indicator lights on the control panel of the way-wolf boiler:

Red flame out, blue low water light, and white power-on light

Utilizing MWT, boiler water is maintained within set parameters. These parameters are:

- Alkalinity testing (pH): 8-11.5

- Total dissolved solids (TDS): below 1,000 ppm

- Chloride: less than 10 ppm

Vacuum/Gravity design provides the most efficient and effective means of separating oil from water

A manual valve, located at the bottom of the vessel, is provided for draining the vessel and for dumping the accumulated solids and sludge from the solids sludge collection chamber. (OWS)

Vacuum/Gravity Two-Stage OWS has 3 indicator lights

- Red light: illuminates when the control power is on

- Amber light: illuminates when oil is being discharged from the system

- Green light: illuminates when water is being discharged from the system

Disadvantages of hydraulics

- Initial installation expense and components replacement cost are high

- Hydraulic fluid can be flammable and hazardous

- Hydraulic fluids operate at high pressures

Pascalâ€™s law â€“ â€œPressure applied to a confined fluid is transmitted undiminished in all directions and acts with equal force on equal areas and at right angels to themâ€

Inside a cylinder there are two working surface areas.

The first is the cap end. Hydraulic pressure working on the cap end area forces the piston rod to extend. The second is the net area.

There are two types of rotary actuators

- hydraulic motor

- rotary actuator

Types of motors

- gear motors

- vane motors

- piston motors

3rd test.  This test has lots of alignment and lubrication questions. I could not remember them all but I answered one, flat table or something. I couldnt find the corresponding info in the course materials.

Notices remain in effect until date of cancellation and are automatically cancelled after

1 year

Done when 50% or more of the original text or when the signature page is changed is a ?

REISSUE

On a Boat Inspection Reports: The report must be submitted not more than ___ days after it is completed.

10

Cutter Engineering Reports Section III and IV include what?

SECTION III â€“ MACHINERY/ELECTRICAL

SECTION IV â€“ ADMINISTRATIVE

SECTION V â€“ CUTTER ENGINEERING SUMMARY

Provide the hours of operation since the last major overhaul for all diesel engines and gas turbines in

Section VI

If a full power trial has not been attempted for over two reporting periods as determined by cutter PMS, provide reasons in

Section VI

Pertinent identifying information about the CASREP equipment item being reported on is found in the _____ information set.

PARTSID

CASREPs must include AIG Six Eight Four Two or AIG Six Eight Four Three as _________ addressees so that CASREP data can be electronically entered into the Navy and Naval Inventory Control Point (NAVICP) databases.

INFO

Shell and tube heat exchangers are used primarily with __________________.

INTERNAL COMBUSTION ENGINES

If the fluids drained from the heat exchanger are considered hazardous materials (HAZMAT), they must be handled IAW applicable federal, state, and local ________.

REGULATIONS

Before conducting a thorough cleaning of a heat exchanger, conduct a preliminary ______________.

INSPECTION

What is the best method for cleaning tubes in a shell and tube heat exchanger?

HIGH PRESSURE WATER JET

What is NOT an advantage of firetube boilers?

â€¢ Inexpensive to build. â€¢ Simple to operate. â€¢ Less maintenance (distractor answer here)

Sensible heat causes a change in temperature, latent heat does not cause a change in temperature.

(KNOW DIFFERENCE)

On auxiliary boilers, permanent magnets project a strong magnetic field. The field acts as a â€œstator,â€ and the feed pump provides the energy to move the liquid _________________.

ARMATURE

The driving force moving the feedwater is the difference in _________between the stages with each stage being at a lower __________ than the one before it.

PRESSURE

On a flash type evaporator, the distillate water passes through a _____________________.

THREE WAY SOLENOID

One question about the first stage and the sixth stage, DONâ€™T REMEMBER IT !!

Before operating a flash type evaporator, personnel should be thoroughly familiar with

the _______________.

DISTILLING CYCLE

When cleaning a flash type evaporator, yellow acid water means _______________.

DISSOLVED AND HEATED

To establish if there is an air leak in the OWS :

PERFORM HYDRSTATIC TEST ON SUCTION PIPING & VERTICAL CYLINDER VESSEL

In an OWS, if the discharge pressure is too high, check for ________________.

FLUID VISCOSITY TOO HIGH

Hydraulics:

AREA = FORCE/PRESSURE

Also referred to as stored energy, ______________ is present in a hydraulic system.

POTENTIAL ENERGY

The three main types of hydraulic accumulators are spring and weight loaded and ______________.

GAS CHARGED

Internal leakage occurring around the seals or the unit if the walls are scored causes _______________.

CYLINDER CREEP

What piece of information are you likely to find on the name plate of an electric motor?

HERTZ

Never operate, repair, adjust, or otherwise tamper with any of the cutterâ€™s electric or electronic equipment without demonstrating, to the _______________.

DIVISION OFFICER

The first step in replacing a switch is to _________________________.

TAG OUT THE CIRCUIT

____________________ are electromechanical devices that require physical contact between a target object and switch activator to make the contacts change state.

LIMIT SWITCH

The supervisor shall be responsible for receipt, inventory, and ______________ of parts and long lead-time material.

INSPECTION

The internal engine overhaul (documentation) shall be maintained on board the cutter until________________________________.

THE NEXT OVERHAUL IS ACCOMPLISHED

_________________________________ before you start working on an engine.

DISABLE THE START CIRCUIT AND DISCONNECT STARTER

Prior to disassembly, check the _________________ alignment between the engine

and the flexible coupling.

FACE AND BORE

Overheating can cause ________________of the lube oil which will leave carbon deposits on the rings and in the grooves.

OXIDIZING

_____________________ are mounted on the crankshafts of some engines to reduce the torsional vibrations.

VIBRATION DAMPENERS

The amount of deflection of a crankshaft may be determined by the use of a _______________.

STRAIN GUAGE

Corrosion of bearing materials causes a chemical action of __________ lubricating oils.

OXIDIZED

An appropriate method to account for shaft droop utilizes a load ring, _____________, and sling.

TURNBUCKLE

______________ or face misalignment occurs when the centerlines of the marine transmission and companion flanges are not parallel.

ANGULAR

_______________ refers to the distance the driving bore of a hub is out of parallel with the shaft centerline.

BORE RUNOUT

_______________ refers to the distance the face of the hub is out of perpendicular to the shaft centerline.

FACE RUNOUT

Use a __________________ to check angular alignment.

FEELER GUAGE

The following are potential causes of propulsion gear failure:

â€¢ Poor teeth contact. â€¢ Inadequate lubrication â€¢ Foreign objects  __(distractor here)_

Always check the gear tooth alignment after a major overhaul, or if the ship has been aground or if the _________________ has been disturbed.

SHAFT ALIGNMENT

Bearing inspections at other than scheduled intervals may be required if:

CONDUCTING A GEAR TOOTH MESH CHECK (read 3-40)

No inspection plate, connection, fitting, or cover that permits access to the gear casing should be removed without specific authorization by the __________________.

ENGINEER OFFICER

When should a final alignment of propulsion engines to shafting be attempted?

WHEN THE VESSEL IS IN THE WATER

Which of the following failures DOES NOT cause low oil pressure in a propulsion transmission?

STUCK REGULATING PISTON IN THE SELECTOR VALVE ASSEMBLY

Drills and exercises shall not begin until permission has been obtained from the commanding officer or ________________ for after-hours duty section drills/exercises.

OFFICER OF THE DECK

In planning and preparing even minor simulated casualties, consideration must be given to the possibility that the simulation could create an ______________________.

ACTUAL HAZARDOUS CONDITION

After completion of each drill or actual casualty, a ___________ is to be conducted .

CRITIQUE

Which risk assessment program uses color coding?

GAR RISK ASSESSMENT MODEL

During the walk-through, one of the safety items that you should identify is the ________________ in the spaces where the drill will be conducted.

HEAT INDEX

What is the MAXIMUM numerical score that should be used on the exercise evaluation sheets?

100

Exercise evaluations will be maintained by the training officer for a MINIMUM of how many years after the exercise has been completed?

2 YEARS

To be a successful SUPERVISOR, you must be able to train and develop others.

One of the greatest contributions you can make as a supervisor is the development of your people.

MLC will decide whether to EXTEND (OR SHORTEN) the overhaul based on the engine condition.

Always shut down the engine before carrying out repairs or adjustments to the engine and driven machinery.

FUEL, WATER, and TEMPORARY BALLAST TANKS are filled to normal average operating levels, generally ½ to ¾ filled.

TO CHECK BORE ALLIGNMENT take measurements of the diameter gap at four equally spaced points on the flanges diameters, A,B,C, and D.

When should you NOT attempt to make a final alignment of propulsion engine/shafting?

WHEN fuel, water, and temporary ballast tanks are empty

The flashing of the feedwater occurs when the psi in the flash chamber is lower than the saturation psi of the feed temp.

A copy of all drill plans should also be included among departmental training records.